CPAP Hose Lift version 5.5

Specification Data Sheet

May 2017

Components:

- strung and ordered together: segmented tubular base with integral tubular mast having top loop for suspending cpap hose.   one piece integral segmented assembly practically self erects.

- plastic hook, mounted upon mast, for mask storage.

- pictorial instruction card.

- fabric travel bag, with drawstring closure and barcode tag.

- new and enhanced with HLv5.5: 14% larger base, 11%, 12% lighter, 16% more compact, barcodes, redesigned molded fiberglass-nylon deep socket mast connection, and added mast to base cord lock feature.

Base

- rectangular, molded fiberglass and anodized aluminum tubular segments; size: 7” x 7.5” x  3/8”  (18 x 19 x .95 cm), all black. product label with manufacturing data affixed to base.  base inserts under, and is held by the weight of: any mattress system, or other weighting object. new v5.5 base: 14% larger; redesigned molded fiberglass-nylon deep socket mast connection, and added mast to base cord lock feature.

Mast

- anodized (light blue) aluminum tubular segments, having machined anodized (clear) aluminum end fitting connections which insert into adjacent segments; an upper segment with 15 and 25 degree bend to achieve reach; all segments held in order and erection sequence by an interior tensioned shock cord; tubing diameter: O.D. 3/8” (9.5 mm); I.D. 5/16” (8 mm).

- loop at uppermost end of mast:  formed from same shock cord within tubular segments, black cord approximately 1/8” (3 mm) in diameter; a black plastic “curly cord” applied onto the cord loop acting as a roller for the cpap hose to move more freely, as cpap hose is held suspended above the patient in bed.

- mast to base connection:  molded fiberglass deep socket base segment receiving lowest mast segment; mast assembly shock cord knotted beneath female socket of base segment, attaching mast to base in one integral assembly.

Instruction Card

- tri-fold paper, 5.83” x 8.27” (14.8 x 21 cm A5), with photographic pictorial of instructions for: assembly, use, and disassembly; folded card and product is held packaged within a rubber band.

Fabric Travel Bag

- approximately 2.2” in diameter x 7.2” long (5 cm in diameter x 18 cm in length), 300 denier polyester; drawstring closure with spring actuated clasp; all black.

- affixed to drawstring: product barcode tag with brief product category description, and  product colored logo on reverse tag side, to that of barcode.

Overall Specifications

- erected height: approximately 41” (104 cm).  new v5.5 mast: optional height( - ) and reach( + ) by reverser bends.

- collapsed travel size: approximately 2.1” in diameter x 7” long (5 cm in diameter x 18 cm in length). new v5.5:  16% more compact.

- total weight with all components including travel bag:  5.7 ounces (156 grams). new v5.5: 12% lighter.

Standard Packaging:

- Cardboard cartons, 10” x 8.5” x 10” (26.5 x 21.5 x 26.5 cm), 10 lbs (4.5 kg), two adjacent sides printed with: manufacturing data and carton (case) barcode.  new v5.5: 12% smaller carton size and, added barcode.

- 25 CPAP Hose Lift “Units” per carton, sealed closed with packing tape.

Manufacturer’s Data

- Arden Innovations, 1280 County Road 100, Georgetown, TX 78626, USA.

- CE mark #CA011750; HTS # 9019.20.00.00; USA: Insurance Code DME 1399, NPI#: 1467684712, Product category: # 15.0266.0819 Sleeping Aids (non prescription).

- Model (Part Number):  CPAPHLv5.5; UPC-A: 859596003014.  Carton ITF-14: 10859596003014

Manufacturer’s Suggested Retail Price

- per CPAP Hose Lift Unit for 2017+:       $36.50  US Dollars each.